## Slide 1: Smart Vehicles Hardware and Processors
Advisor: Hassan Rajaei
Presented by: Aakanksha Mahajan, Anusha Allu and Sampath

## Slide 2: Introduction
What is a Smart Vehicle?
A Smart Vehicle is defined as a collection of various smart IoT devices which are connected to a network and effectively communicate with each other for providing a good travel experience for the user(s).

## Slide 3
RQ1: How does communication take place using V2V and V2I?
RQ2: How does distributed and parallel communication takes place in smart vehicles?
RQ3: How reliably can communication help enhance efficiency and accuracy in smart connected cars and avoid failure?
Research Questions

## Slide 4
Notes: Here we can oberserve in this picture that therea are many possibilities that a smart car can communicate with various other smart entites which are connected to a network.
This communication can be extabloished using one of most emergig technology which is known as VANETs.
Under the classification of VANETs we have various types of communications: V2V, V2I, V2P etc
In this presentation we maily foucs on how communication takes place in V2V and V2I techniques.

## Slide 5
Vehicle-to-Vehicle Communication:
Vehicle-to-Vehicle (V2V) Communication is a most recent and advanced approach where smart cars talk or share information with each other electronically in real time. This sharing of information helps the smart vehicle to provide safety and a good travel experience.
Vehicle-to-Infrastructure Communication:
Vehicle-to-Infrastructure (V2I) Communication is also an advanced technology in VANETs which aims at establishing communication between the smart car and the Road Side Units (RSU).
What is V2V and V2I Communication?

## Slide 6: How V2V and V2I Communication Work?
Vehicle-to-Vehicle and Vehicle-to-Infrastructure Communication basically works on the principle of Distance Short-Range Communication (DSRC).
Dedicated Short-Range Communication is a new way of establishing communication which uses 75MHz frequency of spectrum which is allowed by the standards of Federal Communication Commission (FCC).
This communication helps to increase the safety of the traveler, fuel consumption is reduced and pollution as well.

## Slide 7
SDN-MEC Architecture Support
Notes: Explain Here for establishing the communcation between the vehicles or the RSU, we follow an architecture which is designed by integrating the newly emerging technology 5G and the Mobile Edge Computing (MEC).

## Slide 8
Smart Vehicles 'x' and 'y' use cellular network to communicate.
SDN Controller of the SDN-MEC server finds a path for communication?
Notify both the smart vehicles to switch from cellular to V2V VANET offloading using V2V path.
Smart Vehicles 'X' and 'y' communicate using theV2V path.
Maintain a Life-Time Session for future purpose.
Flow of Establishing Communication

## Slide 9
5.9Ghz DSRC Transmitter.
This hardware works on IEEE 802.11p.
Components included:
  Programable Gain Amplifier.
  Drive Amplifier.
  Serial Peripheral Interface.
Hardware Support for DSRC

## Slide 10
CASE STUDY
Vehicle-to-Vehicle Communication using Visible Light Communication (VLC).
Includes two key components for sharing information between the Smart Vehicles or Road Side Units (RSU).

## Slide 11
CASE STUDY
Transmitter (Leading Vehicle):
  Laptop
  Universal Software Radio Peripheral (USRP).
  Front-end Board.
  Tail Light.
Receiver (Following Vehicle):
  GPS Receiver.
  Universal Software Radio Peripheral (USRP).
  LIDAR.
  Antennas.

## Slide 12
As per today on an average there are 60-100 sensors in a car.
It is estimated that a car will have 200 sensors on an average.
GPS
LiDAR
Radar
Ultrasonic
Video Cameras
Central Computing System
Sensor Information

## Slide 13
Real Time Data Processing

## Slide 14: Reliability of communication between the vehicles and the infrastructure
Data Age MAC scheme which ensures reliable communication between the vehicles using the concept of platoon of vehicles. This scheme is like an alternate to the standard IEEE 802.11p standard.
Reliability and Performance Statistics with example how V2V communication is proving to be reliable using the use case of predicting crash or collisions of vehicles.

## Slide 15: Reliability of communication between the vehicles and the infrastructure
Data Age MAC scheme

## Slide 16: Reliability of communication between the vehicles and the infrastructure
Data Age MAC scheme

## Slide 17: Reliability of communication between the vehicles and the infrastructure
Data Age MAC scheme

## Slide 18: Reliability of communication between the vehicles and the infrastructure
Reliability and Performance Statistics of V2V communication

## Slide 19: Reliability of communication between the vehicles and the infrastructure
TTC error without V2V (33.6%) is higher than using V2V data (21.66%)
Mean Vx error using V2V data is smaller (5%) when compared to the mean error (14%) using sensors.
Reliability and Performance Statistics of V2V communication

## Slide 20: Parallel and Distributed Communication in Vehicles

## Slide 21
In-Vehicle Communication Architecture
Few network protocols used in Vehicle communication are:
LIN (Local Inter-Connect Network)
CAN (Controller Area Network)
FlexRay
MOST (Media Oriented Systems Transport)

## Slide 22
Intra- Vehicular Wireless Sensor Networks
CAN bus is not flexible to handle a greater number of sensors
Wireless architectures help in such scenarios
Various sensors in the vehicle share the data that sensors generate to develop a smart car
ZigBee, RFID, WiFi, and Bluetooth can be used to make use of IoT

## Slide 23
Future Intra Vehicular Network Architecture
Parallel Communication in Intra-Vehicles

## Slide 24
Parallel Communication in Intra-Vehicles
Possible partitioning for Multicore components
Multicore systems can be used
Software components must be integrated with less ECUs
Use of Large-Scale Software Integration techniques

## Slide 25
Intel Atom Automotive Processors
Intel Field Programmable Gate Arrays (FPGAs)
GPUs
Arm Multi Core Processors
Processors for Automobiles
Parallel Communication in Intra-Vehicles

## Slide 26
Example
Arm releases Cortex A76AE processor for automobiles in December,2018
Dual core allows to gain high performance
Different clusters of CPU cores are responsible for different work load tasks

## Slide 27
5G
Mobile Edge Computing (MEC)
SDN – Software Defined Networking
NFV – Network Function Virtualization
Network Slicing
Distributed Communication in IoV

## Slide 28
Internet of Vehicles
Evolution of CIoV

## Slide 30
Cognitive Internet of Vehicles
Architecture of CIoV

## Slide 31
Healthcare in Autonomous Vehicles
Example of CIoV

## Slide 32: Conclusion
V2V Communication is reliable.
V2V and V2I Communication can be implemented with the support of SDN-MEC Architecture.
The newly emerging 5G technology helps in enhancing fast communication which helps the smart vehicles to make quick decisions and provide user(s) a good travel experience by maintaining safety.
Latest processors like ARM multi core processor can be used to achieve parallel programming inside vehicles
Using Edge Computing, distributed communication can be achieved